## Slide 1: Driving Fundamentals
Unit D

## Slide 2: Driving Fundamentals
Successful Driving
Operational Skills- Drivers must have the skill set needed to safely operate the school bus.
Vehicle Awareness- Drivers must constantly be aware of the dimensions of the school bus and understand its operation.

## Slide 3: Types of School Buses
Type A1- Entrance door behind front wheels 10,000 lbs. or less
Type A2-Entrance door behind front wheels, greater than 10,000 lbs.
Type C- Utilizes a chassis with a hood and front fender assembly, entrance door is behind the front wheels
Type D- Constructed utilizing a stripped chassis, entrance door is ahead of the front wheels

## Slide 4: Fuel Types of Schools Buses
Electric
Propane
Diesel
Gas

## Slide 5: School Bus Size
Bus Type | Type A | Type C | Type D
Weight | Up to 10,000 | 18,000 to 35,000 | 27,000 to 37,000
Height | 9.1 feet | 9.9 ft. to 10.4 ft. | 9.9 ft. to 10.4 ft.
Width | 93 inches | 93 to 96 inches | 93 to 96 inches
Wheelbase | 138 inches | 149.6 to 276 inches | 136 to 276 inches
Turning Radius | 25 feet | 23 to 38 feet | 21.3 to 34.24 feet
Length | 13 to 17.5 feet | 20.9 TO 38.9 feet | 27.3 to 39.11 feet

## Slide 6: Starting The Bus
Adjust the driver’s seat and mirrors
Fasten seatbelt
Set the parking brake and place transmission in neutral
Turn ignition key to the right to check gauges

## Slide 7: Checking The Gauges
Oil- Check operation (see owner’s manual)
Fuel- At least ½ full, ideally tank should be full
Air pressure- 100 + lbs. per square inch
Voltmeter- Check for operation
Engine Temperature- Check for operation
Notes: ABS, ? ??

## Slide 8: Starting and Accelerating
Apply service brake and release parking brake
Place bus in “Drive” for an automatic
Check mirrors for approaching traffic and signal your intentions
Depress accelerator

## Slide 9: Smooth Stopping
Requires you to think and plan
Total stopping distance= Perception distance + Reaction distance + Brake lag + Braking distance

## Slide 10: Braking
Braking distance changes with road conditions and speed
Braking distance is longer on a wet surface than a dry surface
Braking distance at 40 mph is four times longer than at 20 mph
As speed doubles, braking distance increases by 4

## Slide 11: Steering and Turning
Driver’s must assume the correct steering position
Prepare for turns by looking ahead 12 to 15 seconds
Use your mirrors and make turns smoothly and correctly by using the proper steering method

## Slide 12: The Perfect Turn
The perfect turn is when the entire bus clears the curb at the corner and the bus stays as nearly as possible in its own lane

## Slide 13: Making a Right Turn
Check the traffic surrounding the bus
Give ample signal for the current speed and distance
Move to the far right hand lane and slow down
Observe and obey all traffic signs and signals
Reduce speed to 10 mph or less, turning slowly gives the driver and others time to avoid problems
When making a turn, allow sufficient space to avoid running over the curb or striking parked vehicles

## Slide 14: Making a Right Turn
Check for pedestrians and check traffic left and right, yield to all pedestrians and vehicles
Turn wide as needed to complete the turn
Complete the turn and deactivate the signal light if necessary

## Slide 15: Making a Left Turn
Check traffic, signal intention
Move to far left lane or right outer lane if 2 left turn lanes
Reduce speed to 10 mph or less
Judge space to avoid curb & parked vehicles
Check for and Yield to bicyclist & pedestrians
Check traffic left, right and straight ahead
Reach center of intersection and start turn
Deactivate signal light if necessary

## Slide 16: Backing
Activate the four way hazard lights at least 100 feet before stopping
Stop the bus in the proper position to back
Check clearance to sides and overhead
Before and during the backing maneuver constantly check mirrors to see that the way is clear, if ever in doubt do not back
Tap the horn and check mirrors again
Back slowly and smoothly

## Slide 17: Off Set Backing
Off set backing has the same procedures except for the final step
Back slowly and smoothly into the opposite lane until the front of the vehicle has passed the parking boundary

## Slide 18: The Backing Rule
Load Before Backing
And
Back Before Unloading

## Slide 19: Parking
When the bus is parked on level ground or an upgrade, shift the gear to low and turn the front wheels away from the curb
When the bus is parked on a downgrade, shift the gear to reverse and turn the front wheels toward the curb or the edge of the road
Turn off the ignition, remove the key and set the parking brake
Whenever possible the driver should park the bus in a manner that eliminates backing

## Slide 20: Parallel Parking the Bus
Make certain to know the size of the bus you are driving
Signal your intentions with the side you wish to park
Line the bus parallel with the parked vehicle, position the bus about 3 feet away
Activate the four way hazard lights, check mirrors to make certain you are clear to begin backing
With the transmission in reverse slowly begin to back the bus

## Slide 21: Parallel Parking the Bus
Turn the steering wheel hard in the opposite direction you wish to back
Visually check in front of and around the bus often, continue backing the bus until it is predominantly in the parking space
Slowly move forward to straighten the bus out

## Slide 22: Positioning the Bus on the Roadway
Parking lanes are for emergency vehicles or emergency conditions
Drive in the farthest lane to the right when possible
On unmarked roads, position bus to the right of the center of the road
Rural roads may have weak outer edges and soft shoulders
Always use a safe following distance

## Slide 23: Intersections
Give the right of way to all pedestrians
Obey all traffic signs, signals and laws
Approach intersections with caution and observe all surrounding traffic. The driver should be prepared to stop if necessary even though they may have the right of way

## Slide 24: Following Distance Rule
0-40 mph
1 second for every 10 feet of your vehicle
Over 40 mph
Add 1 second
Example 0-40 mph
40 ft. vehicle = 4 seconds
Over 40 mph
40 ft. vehicle = 5 seconds

## Slide 25: Outside Cities and Town
Keep at least 200 ft. behind other trucks and buses NEVER follow another vehicle closer than one bus length
Blind Spots are areas around larger vehicles where crashes are more likely to occur
Blind spots on the side, front and rear also including areas where cars and other vehicles disappear from the driver’s view

## Slide 26: Passing and Being Passed
Generally, the school bus driver will not have to pass another vehicle but when it is necessary, the driver should pass only where it is permitted, pass on the left at a safe distance
Avoid passing or running side by side with another school bus

## Slide 27: Passing and Being Passed
Never pass another vehicle that is weaving or looks to be out of control
When another vehicle passes, stay in the right lane, continue at same speed or decrease and allow the vehicle to pass

## Slide 28: Railroad Crossing
Tap the service brake to alert drivers behind the bus
Activate the 4-way hazard lights and stop the bus within 50 ft. but not less then 15 ft. from the railroad crossing
With the bus stopped, apply the emergency brake and place the gear in park or neutral
Turn off all noisy equipment, open the entrance door and driver window to look and listen for a train in both directions
When safe to cross, close entrance doors and turn off 4-way hazard lights and cross the tracks without changing gears

## Slide 29: Speed Limits for School Buses
The maximum speed limit for school buses shall be 45 mph or the minimum speed allowable, whichever is greater, on any highway where the maximum speed limit is 55 mph or less and 60 mph on all interstate highways and on other highways where the maximum speed limit is more than 55mph

## Slide 30: Driving on School Grounds
Stay alert and proceed slowly and cautiously
Stop at designated place for loading and unloading
Always follow road rules
Never deactivate warning lights when loading and/or unloading
Never pass or allow another vehicle to pass when loading or unloading

## Slide 31: Driving on School Grounds
Check mirrors often before moving
Leave school grounds safely and orderly

## Slide 32: Driving under Special Conditions
Driving conditions vary greatly by location
Special conditions put special responsibilities on the driver. The professional driver modifies driving approaches under unfavorable driving conditions.

## Slide 33: Rural Driving
Drive with caution and reduce speed on narrow roads
Be cautious of wild animals like deer possibly jumping out in front of the bus

## Slide 34: Urban Driving
Be aware of the frequency of intersection and limited escape routes
Speed of the vehicle should be consistent with traffic in the non-accelerate lane

## Slide 35: Expressway Driving
Be certain you are entering the correct ramp
Check traffic around you, signal and search for a gap
Accelerate speed to blend into traffic smoothly
Using caution as you merge, turn off signal and adjust speed

## Slide 36: Driving in Darkness
Prepare the bus by completing a through pre-trip, check and clean headlights, taillights, signal lights and windows
Lights will not help you see better in early twilight, but they will make it easier for other drivers to see you
Always reduce speed and increase your following distance

## Slide 37: Activity Trips
Prepare for a trip by familiarizing yourself with the route
Designate the teacher or coach to maintain safe behavior on the bus
Never allow the emergency exits to be blocked
Always secure loose items
Inform all passengers of emergency procedures and how to use emergency equipment
Stay on schedule

## Slide 38: SIPDE Technique
Search – Search aggressively for potential hazards
Identify – Locate hazards and potential conflicts
Predict- Anticipate how the hazard may affect you
Decide- Determine how to reduce the hazard
Execute- Carry out your decision

## Slide 39: Connect with VDOE
Jackie.Johnson@doe.virginia.gov
Twitter: @VDOE_News Facebook: @VDOENews
#VAis4Learners #EdEquityVA